## Slide 1
GIS Data Types and Data Representations

## Slide 2: Types of Data
  Geographic Location or Spatial Data
  (where is it?)
Spatial Data
Non-Spatial Data
  Attribute data or Non-Spatial Data
  (what is it?)

## Slide 3: Spatial Data
By spatial data we mean data that contains positional values.
Spatial data describes the absolute and relative location of geographic features.
Geographic position specifies the location of a feature or phenomenon by using a coordinate system.

## Slide 4: Attribute Data
Attribute or aspatial or non-spatial data
Data that describes characteristics of the spatial features or data. These characteristics can be quantitative and/or qualitative in nature. Attribute data is often referred to as tabular data.
The attributes refer to the properties of spatial entities such as identity (e.g. maize, granite, and lake), ordinal (e.g. ranking such as class 1, class 2, class 3) and scale (e.g. value such as water depth, elevation, erosion rate).
  They are often referred to as non-spatial data since they do not in themselves represent location information.

## Slide 5: Spatial Data and Attribute Data in GIS come together
Take the example of roads. To describe a road, we refer to its location (i.e., where it is) and its characteristics (e.g., length, name, speed limit and direction). The location represents spatial data, whereas its characteristics are attribute data.
Thus the feature road has two components spatial data as well as attribute data.

## Slide 6
Spatial Data and Attribute Data

## Slide 7
GIS Data Models | Formats | Representations

## Slide 8
As discussed in earlier sessions, geographic phenomena has to be modelled and represented in computer understandable formats in order to process it.

## Slide 9: Data Model / Formats
Vector Data Model
Raster
Data Model

## Slide 10: Data Formats: Vector & Raster
Traditionally spatial data has been stored and presented in the form of a map.
There are two fundamental methods of representing geographical features to preserve geometry. They are:
  Vector
  Raster
Raster and Vector are two methods of representing geographic data in GIS.

## Slide 11: Data Formats: Vector & Raster
Spatial features in a GIS database are stored in either vector or raster form.
Figure |  | Figure
Vector format |  | Raster format

## Slide 12: Vector Data
  Spatial Features are represented as:
    points
    lines
    polygons
Information about a feature is stored in an attribute table.
There can be many different attributes for each feature.

## Slide 13: Vector Data: Point Data
A point is a 0 dimensional object and has only the property of location (x,y).
Points can be used to Model features such as a well, building, power, pole, spot height etc.
However, depending upon scale, other larger objects can also be modelled as vector data.

## Slide 14: Vector Data: Line data
A line is a one-dimensional object that has the property of length.
Lines can be used to represent road, streams, boundary etc.

## Slide 15: Vector Data: Polygon data
A polygon is a two-dimensional object with properties of area and perimeter
A polygon can represent a city, lake, river, etc.

## Slide 16: Vector Data
Many entities can be represented in either point, line or polygon.
The choice depends upon the purpose of representations.
If we are concerned with road width, we need to represent it as polygon.
But if we are only interested in distances, roads can be represented as line.

## Slide 17: Raster Data
Features are represented as square cells in a grid with one value per cell.
Examples of data in raster format - scanned aerial photographs, satellite images and scanned documents or maps.

## Slide 18: Scanned Map

## Slide 19: Satellite Imagery

## Slide 20
Landcover Landuse Maps

## Slide 21
Digital Elevation Model (DEM)

## Slide 22
Digital Elevation Model (DEM)

## Slide 23
Digital Elevation Model (DEM) with Hill Shade

## Slide 24: Choice of Raster and Vector Data Model
The choice of raster and vector data model depends on:
  Type of Geographic Phenomena
  Type of Analysis
  Is also dependent on software algorithm (i.e input requirements and output given by software)

## Slide 25: Choice of Raster and Vector Data Model
The choice of raster and vector data model depends on:
  Type of Geographic Phenomena
  Example : Geographic Field >> Raster Data Model
  Geographic Objects >> Vector Data Mode

## Slide 26: Choice of Raster and Vector Data Model
The choice of raster and vector data model depends on:
  Type of Analysis
  Example : Landuse change >> Raster Data Model
  Network analysis >> Vector Data Model

## Slide 27: Advantages and Disadvantages of Raster and Vector Data Representation

## Slide 28: Conversion of Raster and Vector Data
Point
Line
Polygon
Vector
Raster
Zone of cells
Notes: DRM

## Slide 29: Points as Cells

## Slide 30: Line as a Sequence of Cells

## Slide 31: Polygon as a Zone of Cells

## Slide 32: Conversion : Raster and Vector Data

## Slide 33: Resolution of raster
Each cell reprents an area of 10by 10 mters , the resolution is 10*10 meter
The size of the area that a single raster cell represents is called the raster’s resolution

## Slide 34: TIN
Triangulated Irregular Network
A set of non-overlapping triangles each with a constant gradient.
It is built from a set of locations for which we have a measurement.
Observe that in three-dimensional space, three points uniquely determine a plane, as long as they are not positioned on the same line.

## Slide 36
A TIN is built from a set of measurements for example points of height.
These points can be scattered unevenly over the study area, with areas of more change having more points
Triangles are fitted through three points to form planes
Triangulated Irregular Network (TIN)

## Slide 37
There are many triangulations possible for the same input dataset
The best triangulations are Delaunay
triangulations which have the following
properties:
Triangles are as equal sided as possible
The circumcircle through its anchor points does not contain any other anchor points.
Triangulated Irregular Network (TIN)

## Slide 38: Triangulated Irregular Network (TIN)

## Slide 39: Triangulated Irregular Network (TIN)
A Tin is a vector representation and not an irregular tessellation because:
Each anchor point has a stored geo reference
The planes do not have a stored values (like raster cells have)

## Slide 40
Each plane fitted through three anchor points has a fixed gradient (Slope)
Each plane fitted through three anchor
points has a fixed aspect.
An aspect is the orientation of the slope, for example Northwest or Southeast
Triangulated Irregular Network (TIN)

## Slide 41: Real world to raster/vector data model
The diagram is the representation of the real world and showing differences in how a vector and a raster GIS will represent this real world.

## Slide 42: Exercise
For the list of geographic phenomena enlisted earlier, you need to decide on which model would you choose. Also provide a reason with an example of its use.
Sn | Geographic Phenomena | Example Use | Type of Data Model

## Slide 43
For all the geographic phenomena in a hydrological cycle, what data model would you use depending on the purpose.
Sn | Geographic Phenomena | Example Use | Type of Data Model

## Slide 44: End