## Slide 1: GIS Output

## Slide 2
The output of GIS is presented in form of a hardcopy map or digital visualization.
All the works done in GIS is only successful if the maps/visualization can provide the right message to the audience.
A message to one type of audience could be noise to other type of audience.

## Slide 3
The reduced and generalized, in a scientific way, representation of the whole or part of the Earth onto a flat medium (generally but not necessarily in a paper) is called a map.
Ground Reality
Representation of Reality (Map)
Map

## Slide 4
Types

## Slide 5: Steps of GIS
Data collection
Data Input
Data Management
Data Analysis
Data Dissemination

## Slide 6
Communication in Maps
Reality….
The geographic
environment
Compile
Cartographer
GIS/CAD specialist
Map
Map
Recognize
Select
Classify
Simplify
Read
Symbolize
Analyze
Interpret
Map User
Image
Mental
image
of reality
Map

## Slide 7: Spatial data visualization
Visualization is considered as the translation or conversion of spatial data from a database into graphics.
GIS as a visualization tool, are most effective in communicating spatial data, whether the emphasis is on the location or the distribution of the spatial pattern.
Mostly the end results are generated as soft copy products on the screen of the computer monitor, dynamic visualization via internet on the web or hard copy paper map using a printer or plotter.

## Slide 8
GIS output is most often in the form of a map, and as such, can benefit from principles of cartographic design developed in cartography regarding:
Graphical excellence
Principles of map design
Remember –”Computers do not make good or bad maps – cartographers do!”

## Slide 9: Spatial data visualization

## Slide 10: How to say what to whom and is it effective?

## Slide 11
Map design
Map design is a visual plan to achieve a goal. The purpose of a map design is to enhance map communication.
A well designed map is balanced and interesting to look and can help to communicate the spatial information to the map reader, where as a poorly designed map can confuse the map reader and even distort the information intended by the map maker.

## Slide 12
Map design
The map designer must design a map that must be simple, appropriateness and pleasing appearance and should consider the following issues carefully;
Why are you making map? Prior to making a map, clarify your purpose. The purpose determines what features are included and how they are represented.
Who are your map audience? The map designer and the map user mostly will be different people, and the map user is not necessarily familiar with the information in the GIS - “the data behind the maps.” Knowing the intended audience for your map will help you design it.

## Slide 13
Map design
What is the final medium of your map? The final form of your map –paper, computer monitor (projector), or web will affect its design.
Evaluate your map: Evaluation plays a useful role in making maps.

## Slide 14: Basic Spatial components

## Slide 15: Bertin’s visual variables (1967)

## Slide 16: Perception properties and visual variables
Notes: Attribute values of features are either qualitative or quantitative. Data scales are:
nominal: Qualitative attribute values are different in nature, without one aspect being more important than another (e.g. forms of land use).
ordinal: Qualitative attribute values are different from each other, but there is one singleway to order them, as some are more important/intense than others (e.g. importance of roads).
interval: Quantitative attribute values are different and can be ordered. The distance between individual measurements can be determined (e.g. Celsius temperature scale).
ratio: Quantitative attribute values are different and can be ordered. Distances between individual measurements can be determined and these individual measurements can be related to each other. They also have an absolute zero (e.g. number of visitors).

## Slide 17
Types of Visualizations

## Slide 18: Chorochromatic maps
Also called Mosaic maps
Greek words
Choros = Area; Chroma= Color
Shows nominal values for area through different colors
The map readers get impression of nominal, qualitative differences
This type of map can be prepared easily by using different colors or black and white pattern

## Slide 19: Choropleth maps
Greek words
choros= area Plethos=Value
Ordinal, interval, relative ratio data in aerial unit can be represented
Values that are used to represent area
The values are calculated for the areas and expressed as a stepped surface, showing a series of discrete values.
As these values are represented through area symbols they can only be relative values.
Generally the darker the grey values, the more intense or the higher the densities of the phenomenon.
Eg: population densities per districts,

## Slide 20: Isoline maps
Continuous data (usually at interval or ratio
level) are displayed by lines connecting points
with equal, representative values in the data set
E.g.: contours : equal elevation
isotherms : equal temperature
isochrones : equal (travelling) time

## Slide 21: Isopleths maps
Combination of a choropleth and an Isoline map, in which the isolines form the boundaries of the areal units.

## Slide 22: Proportional point symbol map

## Slide 23: Proportional pie graphs
Circle sizes proportional to total values
Circle sector sizes proportional to corresponding parts of the total

## Slide 24: Prism map (stepped statistical surface)
Areas are represented as elevated spatial units (2.5 / 3D) or prisms
Elevation is proportional to the data values: absolute ratio data, aggregated over areas

## Slide 25: Flowline map
thematic map type in which directions and/or routes of movement are represented by lines / arrows of varying widths
the width of each line / arrow is proportional to the statistical value of the movement along it (e.g. number of vehicles, volume of freight, monetary value of trade)
application of the visual variable size to represent absolute ratio data

## Slide 26: Flowline map

## Slide 27: Dot density maps
Shows the actual distribution.

## Slide 28: 3D map visualization

## Slide 29: Time Mapping

## Slide 30: Urban Growth mapping

## Slide 31: 2D, 3D & 4D Mapping

## Slide 32
Map Layout

## Slide 33: Map Layout
Map layout deals with the arrangements and composition of map elements such as Map body, Map Title, Map Scale, Legend, North arrow, Bibliographic information etc.
Major concerns with layout should have a clear focus to a map body, rest of the part to put in the good order and should look balance as well.
Map layout Tools are available in ArcGIS

## Slide 34: Basic Map Elements
The following are the basic elements of a map;
  Map Title ,
  Map Scale,
  Legend
  North arrow
  Bibliographic information
  Graticule /Grid:
  Border Line and Neat lines
  Map body
  Place names and labeling
These all elements work together to bring spatial information to the map reader.

## Slide 35: Basic Map Elements
The Development regions of Nepal
Scale 1: 500, 000
Modified Universal Transverse Mercator Projection
This map is produced in 1995 by Survey Department, Nepal
0
4
1
2
3
hundreds of
kilometers
Legend
Map Scale Graphical Scale
Bibliographic information
North Arrow
Inset
Map body
Map Projection
Neat line
Border
Title
Central Development region.
Map Index
A B
Map Scale Representative Fraction

## Slide 36
Marginal Information
Additional information to use map properly
  Map title
  Sheet No
  How and when the map was made
  Statement of scale and scale line
  Legend
  Contour interval
  Sheet index
  Declination Figure
  Sheet history
  Copy Rights etc

## Slide 37
Layouts
Layout Title
North Arrow
Scale Bar
Chart
Table
Legend
Data Frame
To insert these objects in a layout, use the Insert menu on the ArcMap document.
Layouts are used to format the final map showing one or more data frames

## Slide 38
Create a map with map elements in ArcMap for the major rivers of Nepal. Add other layers as necessary.

## Slide 39
End of Session